## Slide 1
PROJECT HIS · FRANKFURT UNIVERSITY OF APPLIED SCIENCES
KTC-Vis
An interactive benchmarking dashboard that puts three EIT reconstruction algorithms — ABC1, CUQI8, PNPE2E — side by side, across all seven official KTC2023 difficulty levels.
Guided by Prof. Dr. Martin Simon & Emanuele Pepe
Team: Muzammal · Savani · Bhuva · Paul
01 / 20

## Slide 2
WHY THIS EXISTS
No tool puts all three KTC2023 algorithms in one room.
Electrical Impedance Tomography reconstructs what's inside a tank from current/voltage measurements at its rim only — an ill-posed inverse problem that gets harder as electrodes drop out.
What already exists
pyEIT — a classical EIT toolkit (back-projection, Gauss-Newton, FEM meshing). Focused on the algorithm layer, not on comparing finished submissions. OpenEIT — built for live hardware streaming, not offline multi-algorithm benchmarking.
The gap KTC-Vis fills
Load all three KTC2023 competition submissions, run them on identical data, and interactively compare reconstruction quality, failure modes, and raw measurements — across 7 difficulty levels and 4 phantom samples — in one reproducible dashboard.
02 / 20

## Slide 3
WHAT IT DELIVERS
Five design goals
1 · Reproducibility
Every experiment is a YAML config plus an HDF5 cache — any run is exactly repeatable.
2 · Extensibility
Adding a 4th algorithm means writing one AlgorithmAdapter subclass — nothing else changes.
3 · Multi-dimensional evaluation
18 metrics x 3 algorithms x 7 levels x 4 samples — quality, shape, class accuracy, fit, speed.
4 · Visual explainability
Every metric links to a picture: low SSIM -> spatial map, high voltage residual -> measurement plot.
5 · Measurement-domain visibility
Raw current, voltage and resistance are explorable on their own, independent of reconstruction.
Result
Six dashboard modules, one shared sidebar, 84 benchmark combinations cached once and reused everywhere.
03 / 20

## Slide 4
THE BENCHMARK
The KTC2023 dataset
A shallow circular water tank (23 cm diameter) ringed with 32 stainless-steel electrodes, with plastic and metal cylindrical inclusions dropped in. The task: reconstruct a 256x256 segmented image of water / resistive / conductive regions from electrode measurements alone.
Seven official difficulty levels progressively remove electrodes and measurements to simulate degraded hardware.
Source: Zenodo v3 -- doi:10.5281/zenodo.10986692
Level | Electrodes | Measurements | % of L1
1 | 32 | 2356 | 100%
2 | 30 | 1624 | 69%
3 | 28 | 1404 | 60%
4 | 26 | 1200 | 51%
5 | 24 | 1012 | 43%
6 | 22 | 630 | 27%
7 | 20 | 513 | 22%
04 / 20

## Slide 5
WHAT'S BEING COMPARED
Three algorithms, three philosophies
ABC1
Smoothness-prior reconstruction repaired by a CNN postprocessor. Learning enters after the physics step.
Strong: levels 1-3, fast, clean.
Fails as: ghost inclusions, boundary erosion.
CUQI8
Level-set + total-variation forward model. Pure optimization -- no neural network, needs FEniCS/FEM at every iteration.
Strong: levels 5-7, stable, geometry-aware.
Fails as: missing inclusions (wrong region count).
PNPE2E
End-to-end U-Net + Plug-and-Play Graph U-Net. Learning enters both before and during refinement.
Strong: difficulty-adaptive across all levels.
Fails as: class flips, mask suppression.
Same tradeoff triangle the Fingerprint Radar (M4) visualizes later: fast-and-fragile vs. slow-and-robust vs. balanced.
05 / 20

## Slide 6
HOW IT'S BUILT
System architecture
KTC2023 .mat files
Zenodo v3 -- currents, voltages, ground truth
↓
Reference-Output Path
ReferenceOutputAdapter -- no Docker
Live Docker Path
ABC1 - CUQI8 - PNPE2E containers
↓
↓
Metrics Engine -> HDF5 Cache
18 metrics -- results/{algorithm}/{level}/{sample}
↓
Plotly Dash Dashboard
M1
M2
M3
M4
M5
M6
06 / 20

## Slide 7
HOW TO STAND IT UP
Data & benchmark workflow
Both paths converge on the same cache format -- the dashboard never knows which one produced a given result.
setup_third_party.sh
Clone the three external algorithm repos.
→
stage_dataset.py
Consolidate into data/raw/ktc2023/.
→
validate_data.py
Verify .mat keys, shapes, pixel values per level.
→
populate_cache_from_reference.py
Fast path -- no Docker, instant dashboard data.
→
run_benchmark.py
Full path -- live Docker reconstructions + real runtimes.
→
app.py
Launch -> http://localhost:8050
Fast path
Reads pre-computed reference_outputs/<algo>/level<N>/ -- seconds, no Docker required.
Full path
run_benchmark.py shells out to each algorithm's Docker image, batching by level where supported -- hours, but produces real reconstructions and real timings.
07 / 20

## Slide 8
SIX MODULES, ONE SIDEBAR
Dashboard at a glance
Algorithm, difficulty level, and sample selectors live in one shared sidebar and drive every tab identically.
M1
Reconstruction Explorer
Ground truth vs. one algorithm's output, segmented and error-mapped.
M2
Difficulty Animator
Play levels 1->7 and watch quality curves degrade in real time.
M3
Comparison Grid
All three algorithms, one case, side by side plus a full scorecard.
M4
Fingerprint Radar
9-axis shape comparison of every algorithm's strengths.
M5
Failure Autopsy
Ranked worst cases with an auto-diagnosed A-E failure type.
M6
Measurement Viewer
Raw current/voltage/resistance, independent of any algorithm.
08 / 20

## Slide 9
M1
Reconstruction Explorer
One case, four panels: is this reconstruction any good, and why or why not?
Ground Truth
What: the true phantom, 3-class heatmap. Why: the answer key everything else is judged against.
Reconstruction
What: continuous Viridis heatmap of the raw output. Why: reveals blur/smoothing before it's hardened into classes.
Segmentation
What: the same output on Ground Truth's colorscale. Why: apples-to-apples visual diff, region-finding only.
Error Overlay
What: green/red/blue/yellow per-pixel outcome map. Why: shows exactly where and how the algorithm is wrong.
09 / 20

## Slide 10
M2
Difficulty Animator
Does an algorithm fail gracefully, or fall off a cliff -- and at which level?
Play 1->7 animation
What: GT / segmentation / error images re-rendered per level. How: cached reconstructions, 1.2s/level auto-advance.
7 degradation curves
SSIM, IoU, Dice, Hausdorff, Position Error, Resolution, Runtime -- one line per metric, dashed marker at the current level.
Level context bar
What: % of Level-1 data remaining. Why: ties the abstract level number to a concrete data-loss severity.
Auto commentary
Plain-English verdict per metric, plus the exact level where SSIM first drops below 0.60.
10 / 20

## Slide 11
M3
Side-by-Side Comparison Grid
Which algorithm actually wins on this exact case, and by how much?
3 reconstruction heatmaps
ABC1, CUQI8, PNPE2E rendered together -- no sidebar-flipping needed.
3 pairwise difference maps
What: -2...+2 diverging heatmap per pair. Why: shows if disagreement is boundary jitter or fundamental.
Voltage Measurement chart
What: grouped bar per injection/channel. Why: is a bad result a weak-data problem, not an algorithm problem?
Full metrics scorecard
All 18 metrics, 3 algorithms, best-per-row starred -- the numeric ground truth behind the pictures.
11 / 20

## Slide 12
M4
Fingerprint Radar
One shape per algorithm -- the tradeoff triangle from slide 5, made visual.
9-axis radar
Total/Easy/Hard SSIM, IoU Conductive/Resistive, Speed, Robustness, Voltage Residual, Curr. Sensitivity -- normalised so outward always means better.
Profile mini-bars
Each algorithm's top-3 strongest axes, one glance, no radar-reading required.
Performance heatmap table
Exact normalised score + raw value per axis x algorithm -- the radar's precise companion.
Axes guide legend
Static reference explaining what each axis measures and which are inverted.
12 / 20

## Slide 13
M5
Failure Autopsy
Root-cause a specific bad result -- not just flag that it's bad.
Ranked worst-case list
All cached cases by ascending SSIM -- jump straight to the worst instead of stepping through 84 combos.
Spatial SSIM + confusion matrix
Which pixels, and which class-confusion pattern, drove the score down.
Boundary + measurement polars
Do errors cluster near removed electrodes? Was the raw signal even there to reconstruct?
Auto failure badge (A-E)
With a 'why this badge' bar chart -- the classification is auditable, not a black box.
A - Ghost
FP-dominant
B - Missing
FN-dominant
C - Class flip
Off-diagonal swap
D - Erosion
Shrunk footprint
E - Suppression
PNPE2E-specific
13 / 20

## Slide 14
M6
Measurement Domain Viewer
Is this a bad measurement, or a bad algorithm? 13 panels, algorithm-independent.
Current & voltage (4 panels)
Injected current polar, measured-vs-reference voltage overlay, dV signal, per-pair SNR.
Resistance (5 panels)
R-per-pair, dR anomaly signal, all-injections overlay, mean+-std summary, contact-quality per electrode.
Anomaly & coverage (4 panels)
Per-injection anomaly score, stability (CV), coverage-per-level chart, full polar coverage map.
CSV export
R/V/I for the selected injection, one click -- for offline analysis.
14 / 20

## Slide 15
THE SCOREBOARD
18-metric engine
Image Quality
SSIM SSIM (min / spatial)
Shape Matching
Hausdorff distance Position error Resolution
Class Specific
IoU x 3 classes + mean Dice x 3 classes + mean Confusion accuracy
Measurement Domain
Voltage residual Resistance consistency Current sensitivity
Efficiency
Runtime (s)
Scale
18 metrics x 3 algorithms x 7 levels x 4 samples -- cached once in HDF5, reused across every module.
15 / 20

## Slide 16
WHO USES THIS, AND HOW
Five use cases
The Researcher
“Which algorithm should I trust at Level 6?”
-> M3 + M4
The Debugger
“Why did CUQI8 fail on sample C at Level 5?”
-> M5
The Reviewer
“Show me one reconstruction, start to finish.”
-> M1
The Data Engineer
“Is this a bad measurement, or a bad algorithm?”
-> M6
The Presenter
“How does quality degrade as electrodes drop?”
-> M2
Every one of them
Starts from the same shared sidebar -- no re-loading data between questions.
16 / 20

## Slide 17
UNDER THE HOOD
Environment, Docker & CI
Conda environment
Python 3.10.13 - Dash 2.14.2 - Plotly 5.18.0 - NumPy/SciPy/scikit-image - PyTorch 2.0.1 (CPU) - pyeit - mat73 - torch-geometric - deepinv
Docker
App image: miniconda3 + Docker CLI, controls sibling containers via the mounted host socket. Each algorithm ships its own image (FEniCS lives only inside CUQI8's).
docker-compose
Mounts ./data as a shared cache and /var/run/docker.sock so adapters can launch algorithm containers.
GitHub Actions CI
Conda + mamba setup -> flake8 -> pytest with coverage, excluding Docker-dependent adapter tests from the default run.
17 / 20

## Slide 18
WHERE THINGS STAND
Status & roadmap
Done
- Full data pipeline: loader, subsampler, HDF5 cache - All 3 adapters (reference + Docker) wired - 18-metric engine, all 6 dashboard modules functional - Docker + docker-compose + CI pipeline green
Open
- Test suite is currently placeholder stubs -- highest-priority gap - Full live-Docker benchmark run across all 84 combinations - Runtime figures for CUQI8 still to be captured
18 / 20

## Slide 19
WHO BUILT THIS
Team & course
Project HIS -- Frankfurt University of Applied Sciences -- guided by Prof. Dr. Martin Simon & Emanuele Pepe
Name | Student ID | Role | Modules
Muhammad Muzammal | 1541353 | EIT & Data Specialist / Backend | M1, M5
Smit Savani | 1420825 | Metrics & Backend Engineer | M3, M6
Asmita Bhuva | 1541650 | Viz & Frontend Developer | M4, M5
Shimul Paul | 1441927 | Integration & DevOps Lead | M2, M6
19 / 20

## Slide 20
TRY IT
Quick start
# 1. environment
conda env create -f environment.yml
conda activate ktc-vis
# 2. populate the cache (fast, no Docker)
python scripts/populate_cache_from_reference.py
# 3. launch
python app.py # -> http://localhost:8050
Thank you -- questions welcome.
20 / 20